How to Install Arches

Follow the Steps Below for outside mounted arches

Step 1. Place arch over window opening being sure that it is centered and the bottom is at the correct location.

Step 2. Insert screw (#6 sheetrock) at top of arch, into pre-drilled mounting hole making sure not to over tighten.

Step 3. Place a level at the bottom of the arch and ensure that it is properly aligned.

Step 4. Insert remaining screws (supplied).

Step 5. Place button caps (supplied) over screw holes and push in as far as possible by hand. Use a small hammer to lightly tap in the rest of the way being careful not to damage the button cap .For Custom colors use supplied touch up paint for cap color.

Step 6. Use a mild window cleaner to remove any fingerprints or dirt. Do not spray directly onto arch or rub hard as this could damage the paint.

For Inside Mounted Arches see website “How To” Install inside mounting strips

rev. 1-1-19

# Text boxes

1 5/8” lg. Sheetrock Screws for Mounting Arch to Sheetrock (om)

1” lg. Sheetrock Screws for Mounting Arch to Mounting strip (im)

1 5/8" lg. Flat Head Screws for Mounting Strip to sheetrock (im)

Screw Caps to cover Mounting Screws

Touch up Paint for Custom Colors(to paint screw caps)

Inside Installation Package

Installation Package

Number of Screws and caps will vary depending on size of arch