"How to"

Custom Arch Slat Installation

- Insert slat spring into outer frame of arch

- Insert inter slat pin (with/flange) into small end of slat

- Insert outer slat pin (no/flange) into large end of slat

- Insert arch slat into outer pin hole and press slat outward against spring allowing lower slat pin to go into predrilled enter pinhole at hub.((may need to cut lower pin length to clear lower hub)

Note: Newer outer slat pins with lock maybe used to replace outer slat pins with flange

# Text boxes

Outer Frame of Arch

# OUTER SLAT PIN NO FLANGE

(See Note)

INTER SLAT PIN (W/FLANGE)

SLAT SPRING

CENTER HUB OF ARCH